## Slide 1: Multimodal Feedback Control for Aerial Manipulation
Master Thesis – Final Talk
Felix Graule
Supervised by Prof. Dr. Margarita Chli & Dr. Stefan Leutenegger

## Slide 2: Introduction: Aerial Manipulation Tasks
F. Ruggiero et al., "A multilayer control for multirotor UAVs equipped with a servo robot arm," ICRA 2015
Grasping
D. Brescianini et al., "Design, modeling and control of an omni-directional aerial vehicle," ICRA 2016
Fetching
K. Bodie et al. “An Omnidirectional Aerial Manipulation Platform for Contact-Based Inspection.” ArXiv 2019
Pushing

## Slide 3: Introduction: Aerial Manipulation Applications
Trujillo et al., “Novel Aerial Manipulator for Accurate and Robust Industrial NDT Contact Inspection: A New Tool for the Oil and Gas Inspection Industry”, Sensors 2019
Inspection
M. Tognon et al., "A Truly-Redundant Aerial Manipulator System With Application to Push-and-Slide Inspection in Industrial Plants” RAL 2019
C. Korpela et al., “Towards valve turning using a dual-arm aerial manipulator”, IROS 2014
Remote Interaction
Maintenance

## Slide 4: Introduction: Research Gap
Recent advances focus on fully-actuated MAVs
Under-actuated MAVs cheap and widespread
Plug-and-play End Effector extension

## Slide 5: Introduction: Hybrid Force and Position NMPC Applied to Aerial Writing
Hybrid nonlinear model of combined MAV-arm system
Considers contact forces acting on End Effector
Models moments caused by CoM displacement
Figures, method and results taken from RSS submission (under review, double-blind) “Aerial Manipulation Using Hybrid Force and Position NMPC Applied to Aerial Writing” D. Tzoumanikas, F. Graule, Q. Yan, D. Shah, M. Popovic, S. Leutenegger
Fig. 1: The aerial manipulation platform used in the ‘Aerial Writing’
experiments with labels for its individual components.

## Slide 6: Introduction: Hybrid Force and Position NMPC Applied to Aerial Writing
Figures, method and results taken from RSS submission (under review, double-blind) “Aerial Manipulation Using Hybrid Force and Position NMPC Applied to Aerial Writing” D. Tzoumanikas, F. Graule, Q. Yan, D. Shah, M. Popovic, S. Leutenegger
Fig. 2: Video summarizing extensive real-world experiments of aerial manipulator while external positioning is used.

## Slide 7: Introduction: Contributions
Appearance-based Precision Evaluation for Aerial Writing
I
II
III
Multimodal Feedback for Aerial Writing
Simulation of Aerial Writing for Evaluation

## Slide 8: Contribution I: Appearance-based Precision Evaluation for Aerial Writing
ICP-based visual error to evaluate drawing on Whiteboard
Independent of noise and biases in external pose measurements
Fig. 3: Visual error between the reference and actual tip position for real-world experiment.
Figures, method and results taken from RSS submission (under review, double-blind) “Aerial Manipulation Using Hybrid Force and Position NMPC Applied to Aerial Writing” D. Tzoumanikas, F. Graule, Q. Yan, D. Shah, M. Popovic, S. Leutenegger

## Slide 9: Introduction: Three Key Limitations of existing NMPC pipeline
MAV Pose
provided externally
Whiteboard Orientation
sensitive to calibration
Delta Arm Model
not adaptive to offsets
1
2
3

## Slide 10: Contribution II: Multimodal Feedback for Aerial Writing
MAV Pose
provided externally
MAV Position Drift Estimator
Whiteboard Orientation
sensitive to calibration
Whiteboard Orientation Estimator
Delta Arm Model
not adaptive to offsets
Relative End Effector Position Control
1
2
3

## Slide 11: Multimodal Feedback: Coordinate Frames
MAV body , Arm , End Effector , Camera , World / , Touch /
Fig. 4: The different coordinate frames used in this presentation.

## Slide 12: Multimodal Feedback: Notation
Position of point with respect to Frame
Homogeneous Coordinate Transform from Frame to
Rotation Matrix from Frame to
Estimate of true value
Measurement of true value z

## Slide 13: Multimodal Feedback: Simulation of Aerial Writing
Simulator based on Gazebo and RotorS
Virtual Hexacopter MAV
Accurate replica of Delta Arm with simulated servos and force sensor
Virtual camera
Simulate writing by moving line segments
Fig. 5: The aerial manipulation platform used in the ‘Aerial Writing’
simulations with labels for its individual components.

## Slide 14: Multimodal Feedback: Simulation of Aerial Writing
Fig. 6: The MAV-arm system performing an ‘aerial-writing’ task in real-life.

## Slide 15: Multimodal Feedback: Simulation of Aerial Writing
Fig. 7: The MAV-arm system performing an ‘aerial-writing’ task in simulation.

## Slide 16: Contribution II: Multimodal Feedback for Aerial Writing
MAV Pose
provided externally
MAV Position Drift Estimator
Whiteboard Orientation
sensitive to calibration
Whiteboard Orientation Estimator
Delta Arm Model
not adaptive to offsets
Relative End Effector Position Control
1
2
3

## Slide 17: Multimodal Feedback: MAV Position Drift Estimator Key Idea
Onboard SLAM system provides drifting position estimate
Simulate and model drift as reverting-mean random walk
Fuse visual and tactile feedback in EKF
Apply to MAV pose used by NMPC
Fig. 8: Simulated drift on axis using mean-reverting random walk.

## Slide 18: Multimodal Feedback: MAV Position Drift Estimator Extended Kalman Filter Definition
State vector: Per axis position drift estimate expressed in World frame
Estimate MAV pose in non-drifting World frame
Prediction

## Slide 19: Multimodal Feedback: MAV Position Drift Estimator Visual Measurement
Reference drawing on Whiteboard What should have been written so far?
Fig. 9: Reference drawing on Whiteboard at current time.

## Slide 20: Multimodal Feedback: MAV Position Drift Estimator Visual Measurement
Reference drawing on Whiteboard What should have been written so far?
Project into estimated camera and masked What should the camera be seeing now?
Fig. 10: Reference drawing projected into virtual camera and masked out.

## Slide 21: Multimodal Feedback: MAV Position Drift Estimator Visual Measurement
Reference drawing on Whiteboard What should have been written so far?
Project into estimated camera and masked What should the camera be seeing now?
Current camera frame What is the camera actually seeing now?
Fig. 11: Current frame perceived by the camera.

## Slide 22: Multimodal Feedback: MAV Position Drift Estimator Visual Measurement
Reference drawing on Whiteboard What should have been written so far?
Project into estimated camera and masked What should the camera be seeing now?
Current camera frame What is the camera actually seeing now?
Compute mismatch using Template Matching How far off is the camera?
Fig. 12: Illustration of visual measurement in pixel space with
camera frame overlaying rendered template image.

## Slide 23: Multimodal Feedback: MAV Position Drift Estimator Visual Measurement
Visual EKF innovation

## Slide 24: Multimodal Feedback: MAV Position Drift Estimator Tactile Measurement
End Effector
Contact Condition
Solve for
Tactile EKF innovation

## Slide 25: Contribution II: Multimodal Feedback for Aerial Writing
MAV Pose
provided externally
MAV Position Drift Estimator
Delta Arm Model
not adaptive to offsets
Relative End Effector Position Control
1
3
Whiteboard Orientation
sensitive to calibration
Whiteboard Orientation Estimator
2

## Slide 26: Multimodal Feedback: Whiteboard Orientation Estimator Key Idea
Assume poorly calibrated Touch frame
Simulate and model miscalibration as fixed orientation error in yaw and pitch
Fuse tactile sensing in EKF
Apply to Whiteboard calibration used by NMPC
Fig. 13: Aerial Writing simulation with actual Whiteboard with orientation offset in white and wrongly calibrated estimate in green.

## Slide 27: Multimodal Feedback: Whiteboard Orientation Estimator Extended Kalman Filter Definition
State vector: Yaw and Pitch offset expressed in World frame
Estimate of non-rotated Touch frame
Prediction
Measurement: Like previous tactile feedback, but use in contact condition

## Slide 28: Contribution II: Multimodal Feedback for Aerial Writing
Whiteboard Orientation
sensitive to calibration
Whiteboard Orientation Estimator
2
Delta Arm Model
not adaptive to offsets
Relative End Effector Position Control
3
MAV Pose
provided externally
MAV Position Drift Estimator
1

## Slide 29: Multimodal Feedback: Relative End Effector Position Control Key Idea
Mismatch in modelled and physical Delta Arm
Simulate as servo angle offsets
Error between model-based command and position
Estimate by fusing AprilTag[1] poses in KF
Define End Effector position error
Fig. 14: The components involved, i.e. the camera (green), the AprilTag mounted on the End Effector and one of the three servos.
[1] J. Wang and E. Olson, "AprilTag 2: Efficient and robust fiducial detection," IROS 2016
D. Malyuta. “Guidance, Navigation, Control and Mission Logic for Quadrotor Full-cycle Autonomy.”, 2018.

## Slide 30: Multimodal Feedback: Relative End Effector Position Control End Effector Position Control
Map to angle offsets using Delta Arm Jacobian
Local feedback loop for Delta Arm cascaded around NMPC
Fig. 15: Overview of simulated tactile measurement hardware.

## Slide 31: Contribution III: Simulation of Aerial Writing for Evaluation
MAV Position Drift Estimator
1
Whiteboard Orientation Estimator
Relative End Effector Position Control
2
3

## Slide 32: Results: MAV Position Drift Estimator
Simulate | Drift
Estimate | Drift
Fig. 16: True and estimated MAV Position Drift with Estimator turned on.

## Slide 33: Results: MAV Position Drift Estimator
Fig. 17: Box Plots of Spring and Pen Tracking Errors while simulating MAV Position Drift with Estimator being off (left) or on (right).

## Slide 34: Contribution III: Simulation of Aerial Writing for Evaluation
Relative End Effector Position Control
3
MAV Position Drift Estimator
1
Whiteboard Orientation Estimator
2

## Slide 35: Results: Whiteboard Orientation Estimator
Simulate | Whiteboard
Estimate | Whiteboard
Fig. 18: True and estimated Whiteboard Orientation Offset with Estimator turned on.

## Slide 36: Results: Whiteboard Orientation Estimator
Fig. 19: Box Plots of Spring and Pen Tracking Errors while simulating Whiteboard Orientation Offsets with Estimator being off (left) or on (right).

## Slide 37: Contribution III: Simulation of Aerial Writing for Evaluation
Whiteboard Orientation Estimator
2
MAV Position Drift Estimator
1
Relative End Effector Position Control
3

## Slide 38: Results: Relative End Effector Position Control
Simulate | Servo
Estimate | Servo
Fig. 20: True and estimated Servo Angle Offsets with Estimator turned on.

## Slide 39: Results: Relative End Effector Position Control
Fig. 21: Box Plots of Spring and Pen Tracking Errors while simulating Servo Angle Offsets with Relative Control being off (left) or on (right).

## Slide 40: Contribution III: Simulation of Aerial Writing for Evaluation
MAV Position Drift Estimator
Whiteboard Orientation Estimator
Relative End Effector Position Control
1
2
3
Combine all Error Sources

## Slide 41: Results: Combined Error Simulation and Rectification
Simulate | All
Estimate | All
Fig. 22: True and estimated MAV Position Drift with Estimator turned on.

## Slide 42: Results: Combined Error Simulation and Rectification
Fig. 23: True and estimated Whiteboard Orientation Offset with Estimator turned on.
Simulate | All
Estimate | All

## Slide 43: Results: Combined Error Simulation and Rectification
Simulate | All
Estimate | All
Fig. 24: True and estimated Servo Angle Offsets set with Relative Control turned on.

## Slide 44: Results: Combined Error Simulation and Rectification
Simulate | All
Estimate | None
Fig. 25: Visual Error with All Feedback Components being turned off.

## Slide 45: Results: Combined Error Simulation and Rectification
Simulate | All
Estimate | All
Fig. 26: Visual Error with All Feedback Components being turned on.

## Slide 46: Results: Combined Error Simulation and Rectification
Simulate | All
Estimate | All
Fig. 27: Box Plots with All Feedback Components being turned on.

## Slide 47: Discussion: Key Takeaways
All Error Sources removed effectively
Drastically improved Visual Appearance
Repeatable Method
Achieve millimetre-level Accuracy
Interference between Feedback Components
Loss of Observability when not in Contact
General
Performance
Limitations

## Slide 48: Discussion: Future Work
Evaluation in real-world Aerial Writing Task
Wide FoV Camera for large Drawings
Submit Results
to ICRA 2021
Scale Sensitive Template Matching
Full 6 DoF Estimation
using Dense Tracking
Tight Fusion of Measurements
Planned
Minor Improvements
Long-Term

## Slide 49: Conclusion – Contributions
Appearance-based Precision Evaluation for Aerial Writing
I
II
III
Multimodal Feedback for Aerial Writing
Simulation of Aerial Writing for Evaluation

## Slide 50
Confidential
(under review)

## Slide 51: Questions and Discussion
Confidential
(under review)

## Slide 52
Backup
Backup Fig. 1: Illustration of Visual Measurement Model showing both the expected MAV pose (color, right) and actual MAV pose (greyscale, left)

## Slide 53: Multimodal Feedback: MAV Position Drift Estimator Filter Definition
Multimodal Measurement function
Measurement update
Backup

## Slide 54: Results: MAV Position Drift Estimator
Simulate | Drift
Estimate | Nothing
Backup Fig. 2: True and estimated MAV Position Drift with Estimator turned off.
Backup

## Slide 55: Results: Whiteboard Orientation Estimator
Simulate | Whiteboard
Estimate | Nothing
Backup Fig. 3: True and estimated Whiteboard Orientation Offset with Estimator turned off.
Backup

## Slide 56: Results: Relative End Effector Position Control
Simulate | Servo
Estimate | Nothing
Backup Fig. 4: True and estimated Servo Angle Offsets with Estimator turned off.
Backup

## Slide 57: Results: MAV Position Drift Estimator
Simulate | Drift
Estimate | Nothing
Backup Fig. 5: Visual Error with MAV Position Drift Estimator being turned off.
Backup

## Slide 58: Results: MAV Position Drift Estimator
Simulate | Drift
Estimate | Drift
Backup Fig. 6: Visual Error with MAV Position Drift Estimator being turned on.
Backup

## Slide 59: Results: Whiteboard Orientation Estimator
Simulate | Whiteboard
Estimate | Nothing
Backup Fig. 7: Visual Error with Whiteboard Orientation Estimator being turned off.
Backup

## Slide 60: Results: Whiteboard Orientation Estimator
Simulate | Whiteboard
Estimate | Whiteboard
Backup Fig. 8: Visual Error with Whiteboard Orientation Estimator being turned on.
Backup

## Slide 61: Results: Relative End Effector Position Control
Simulate | Servo
Estimate | Nothing
Backup Fig. 9: Visual Error with Relative End Effector Position Control being turned off.
Backup

## Slide 62: Results: Relative End Effector Position Control
Simulate | Servo
Estimate | Servo
Backup Fig. 10: Visual Error with Relative End Effector Position Control being turned on.
Backup

## Slide 63: Results: Combined Error Simulation and Rectification
Simulate | All
Estimate | None
Backup Fig. 11: Actual Drawing on Whiteboard with All Feedback Components being turned off.
Backup

## Slide 64: Results: Combined Error Simulation and Rectification
Simulate | All
Estimate | All
Backup Fig. 12: Actual Drawing on Whiteboard with All Feedback Components being turned on.
Backup